## Slide 1: Transit Terminal Display
12/4/2025

## Slide 2: Base Station Server
Raspberry Pi running
Custom Python server application accepts TCP/IP connections on port 3141
TCP/IP in
Serial (UART)
Arduino MKR WAN 1310
or
Feather M0 LoRa95
$BSTXT,0A,color|green|\ntext|0|Hello World\n*
$BSTXT,0A,color|green|\ntext|0|Hello World\n*33
LoRa RF
915MHz

## Slide 3: Bus Stop Display
Serial (UART)
Arduino MKR WAN 1310
or
Feather M0 LoRa95
Matrix Portal M4
$BSTXT,0A,color|green|\ntext|0|Hello World\n*
color|green|
text|0|Hello World
LoRa RF
915MHz

## Slide 4: Software Components
Basestation
  Raspberry Pi – basestation.py
  Arduino Sketches (LoRa Module)
  Feather M0 - Basestation-Feather-M0.ino
  Arduino MKR WAN – 1310 - Basestation-MKR-WAN-1310.ino
Bus Stop
  Arduino Sketches (Lora Module)
  Feather M0 - BusStop-Feather-M0.ino
  Arduino MKR WAN – 1310 - BusStop-MKR-WAN-1310.ino
  Arduino sketches (display)
  Matrix-Portal-Display-Driver.ino

## Slide 5: Next Week
Review BOM
Setup of Arduino IDE and programming modules
Review of Solar Power system types of connectors
Antennas and RF cabling
Lightning Protection
Use of site survey equipment (hiker)
Follow on procurements

## Slide 6: Discussion Area and some next steps
Baud rate vs range
Repeat mode (for some bus stops?)
Timing of messaging to avoid collisions in repeat mode
Acknowledgements (ack)
Encryption or RF? tinyAES?
Change LoRa sync word from 0x34 ?
Define what stops repeat to….
Chassis for base station and Bus Stop displays

## Slide 7: Site Survey
Base Station
  Mounting antenna
  Cable runs
  Grounding systems
  Power and internet
  Mounting base station hardware
Bus stop
Panel mounting
Battery box mounting
Bus stop display mounting
Cable runs
Available power?
Security/ vandalism

## Slide 8: LoRa Spectrum (125KHz BW)

## Slide 9: Amazon – inexpensive LoRa Antenna VSWR

## Slide 10: Transit Station Antenna

## Slide 11: Base Station Antenna